## Slide 1
FEM in NX Nastran

## Slide 2
<number>
preprocessing:
mesh generation
material definitions
definition of loads and boundary conditions
postprocessing:
visualisation and analysis of results
(primary and secondary field variables)
solving:
solving the (linear) set of equations
displacement
stress/strain
temperature
acoustic pressure
velocity/intensity
heat flux
…
…
FE technology modelling process
components

## Slide 3
<number>
co-ordinate systems
nodes
elements
geometrical properties
material properties
units
loads and constraints
FE technology modelling process
preprocessing
illustration for NASTRAN (NAsa SRTuctural ANalysis

## Slide 4
<number>
nodes are called GRID points in NASTRAN
grids are defined as points in space that have :
  a unique number (integer)
  a certain location X,Y,Z
    coordinate systems aid in locating point
  6 Degrees Of Freedom (DOFs) to move in space
    coordinate systems aid in interpreting displacement results
FE technology modelling process
preprocessing
nodes
GRID definition statement :
  GRID ID CP X Y Z CD
  where
    ID : identification number
    CP : reference to coordinate system that was used to position the grid
    X,Y,Z : co-ordinates
    CD : reference to coordinate system in which the input (loads, BC) and output (displacements) are defined

## Slide 5
<number>
FE technology modelling process
preprocessing
elements

## Slide 6
<number>
3D Solid Elements | 2D Surface Elements | 1D Line Elements
<none> | Plate/Shell Thickness | Beam orientation (3th point) Beam cross section properties
t
FE technology modelling process
preprocessing
geometry

## Slide 7
<number>
Basic Material Property Definitions :
  linear : deformation are directly proportional to the applied load
  elastic : an elastic structure returns to its original, undeformed shape when the load is removed
  homogeneous : properties are independent of location within the material
  isotropic : material properties do not change with the direction of the material
FE technology modelling process
preprocessing
material properties
MATERIAL definition statement :
MAT1 ID E G NU RHO ... … GE
  where
    ID : identification number
    E : Young’s modulus
    G : Shear modulus G = 0.5 * E / (1 + NU)
    NU : Poisson’s ratio
    RHO : Mass density
    GE : structural damping coefficient

## Slide 8
<number>
most FE solvers do not have an explicit notion of physical units.
it is the user’s responsibility to use a consistent set of units.
popular unit sets : SI, English Units
If the units are not known, try to estimate them from :
  the grid coordinates (if you know the dimensions of the structure, you should be able to deduce the length unit)
  the material definition (for known materials such as steel, aluminum, ….)
Common mistakes in FE models originate from wrong material values (due to wrong unit conversions) !!
FE technology modelling process
preprocessing
units

## Slide 9
<number>
Static Loads :
  concentrated loads applied to grid points (FORCE, MOMENT)
  distributed loads on line elements (PLOAD1)
  normal uniform pressure loads on surface (PLOAD, PLOAD2)
  normal pressure load on face of 2D or 3D element (PLOAD4)
  gravity or acceleration loads (GRAV)
Enforced displacement (SPCD)
FE technology modelling process
preprocessing
loads

## Slide 10
<number>
  RLOAD1 or RLOAD2 statement that refer to
      DAREA statements (spatial definition of load : A )
      2 TABLED1 statements (spectral definition C(f),D(f) real/imag for RLOAD1, amplitude/phase for RLOAD2)
  Selection of dynamic loading with DLOAD case control statement (reference to RLOAD1 / 2 )
Dynamic Loads :
  concentrated loads applied to grid points :
FE technology modelling process
preprocessing
loads

## Slide 11
<number>
a constraint is the enforcement of a prescribed displacement on a single grid point or a set of points
two basic types of constraints :
  single point constraints (SPCs) :
    enforces a displacement (for example zero displacement ) to a single point
  multiple point constraints (MPCs)
    enforces a mathematical constraint relationship between one grid point and a set of grid points
FE technology modelling process
preprocessing
constraints

## Slide 12
<number>
solution sequence for mode calculation
undamped
no external forces
m : eigenfrequencies (# modes = total # dofs n)
m : eigenmodes (each eigenvector has size (nx1))
FE technology modelling process
solver
Lanczos algorithm :
iterative procedure to determine a subset of modes
mode calculation = standard eigenvalue problem

## Slide 13
<number>
solution sequence for dynamic response analysis
1. direct solution method:
2. modal solution method:
solving the FE matrix equation directly for the unknown nodal dofs
dedicated large model solvers that fully benefit from matrix properties
projecting the original dofs onto a modal base
that possibly leads to some substantial model size reduction
back-substitution of result vector {p} into field variable approximation
FE technology modelling process
solver

## Slide 14
<number>
solution sequence for dynamic response analysis
2. modal solution method:
2.1. calculating the undamped modes
m : eigenfrequencies (# modes = total # dofs n)
m : eigenmodes (each eigenvector has size (nx1))
FE technology modelling process
solver
2.2. projection of original dofs onto modal base

## Slide 15
<number>
solution sequence for dynamic response analysis
2. modal solution method:
2.3. construction of modal model
m} : (ma x1) vector of unknown modal participation factors
diagonal matrices due to mode orthogonality !
2.4. solving modal model for unknown modal participation factors m
2.5. back-substitution of result vector into field variable approximation
solver
FE technology modelling process

## Slide 16
<number>
solution sequence for dynamic response analysis
2. modal solution method:
model size reduction: from (nxn) to (maxma)
if ma=n : same accuracy is obtained with direct solution sequence
accuracy depends on size of modal base ma
if ma< n : possible gain in computational effort but loss in accuracy
‘rule of thumb’:
reasonable accuracy at some frequency  requires a modal base that contains at least all modes with eigenfrequencies up to 2
mainly at low frequencies (low modal density)
the required number of modes can be substantially smaller
than the original number of degrees of freedom
FE technology modelling process
solver

## Slide 17
solution sequence for transient analysis
FE technology modelling process
solver

## Slide 18
<number>
overview of some NASTRAN solution sequences:
  SOL 101 : linear static analysis
  SOL 103 : normal modes
  SOL 107 / 110 : complex modes (direct/ modal)
  SOL 108 / 111 : frequency response (direct/ modal)
  SOL 109 / 112 : transient response (direct/ modal)
  SOL 106 : non-linear statics followed by normal modes
  SOL 200 : Design sensitivity and optimization
solver
FE technology modelling process

## Slide 19
<number>
visualisation and analysis of results
(primary and secondary field variables)
displacement
stress/strain
temperature
acoustic pressure
velocity/intensity
heat flux
…
…
FE technology modelling process
postprocessing
! secondary variable approximations are less accurate
then primary variable approximations !

## Slide 20: How to read a nastran file
<number>

## Slide 21
discretization error
idealization error
FE modeller has a determining impact on prediction accuracy
solution error
choice of underlying mathematical model (avoid singularities )
representative boundary condition modelling
appropriate material modelling
mesh quality: balance between accuracy and computational load
(CPU and memory)
choice of solver
representative load modelling
FE technology some practical issues

## Slide 22
avoid singularities
stress singularities
displacement singularities
e.g. stress at sharp re-entrant corners
point (in 2D) or edge (in 3D) connections cannot withstand reaction forces (e.g. spotwelds !)
FE technology some practical issues

## Slide 23
CAD geometry  FE geometry
prior to meshing
defeaturing
idealization (e.g. shell versus solid)
clean-up
FE technology some practical issues

## Slide 24
appropriate meshing
avoid distorted elements
low order p …
low distortion allowed
watch out with automatic meshers
watch out with morphing
FE technology some practical issues

## Slide 25
appropriate meshing
avoid distorted elements
FE technology some practical issues

## Slide 26
appropriate meshing
avoid mesh incompatibilities
induce master/slave relations … no reliable stress evaluation
FE technology some practical issues

## Slide 27
thin hollow plate
horizontal tensile load – constrained at left side
first-order triangular elements
horizontal displacement (p=1)
von Mises stress (p=1)
FE technology some practical issues

## Slide 28
horizontal displacement (p=1)
von Mises stress (p=1)
FE technology some practical issues

## Slide 29
appropriate meshing
solids for bending
not OK
OK
FE technology some practical issues

## Slide 30: Challenges
numerical modelling techniques
mesh generation process
data management
computer resources
enhanced computational efficiency
account for variability
...
automation
(multi-physics) compatibility
re-use of models
exchange, sharing
interpreting, mining
...
...
parallel computing
Data transfer
Meshing
Modeling
Solvers
Post-process
Refinement
0
20
40
60
80
100
NOW
DESIRED
<20%
>50%
increasing “value-added engineering time”
advanced material models
...
morphing

## Slide 31: Some reference books
O.C. Zienkiewicz and R.L. Taylor: ‘Finite Element Method Set’
(ISBN 0470395036 - Butterworth-Heinemann - 2000)
volume 1 : ‘The Basis’
volume 2 : ‘Solid Mechanics’
volume 3 : ‘Fluid Dynamics’
Paul M. Kurowski:
‘Finite Element Analysis for Design Engineers’
(ISBN 0-7600-1140-X - SAE International - 2004)