## Slide 1
Exercise (to be discussed during the oral examination): dynamic analysis of a car chassis
Objective: evaluate the natural frequencies and the accelerations sensed by the passengers due to frequency-dependent loads applied to the suspensions.

## Slide 2
Applied Loads

## Slide 3
Input points (suspensions)
Input | Node ID
FL | 26713
FR | 12052
BL | 17493
BR | 2611
All four loads are applied on the +Z direction;
Loads are imported from the files:
  susp_att_BL.txt
  susp_att_BR.txt
  susp_att_FL.txt
  susp_att_FR.txt
Use the selection filter to select the nodes;
Using the normal view, some points may not be visible: rotate the view to see them.
BL
BR
FL
FR

## Slide 4
File structure
File: susp_att_FL.txt
Column # | Quantity | 
1 | Frequency | [Hz]
2 | Amplitude | [N]
3 | Phase | [deg]

## Slide 5
Response points (seats)
Seat # | Node ID
1 | 25171
2 | 10445
3 | 20197
4 | 5386
1
2
3
4

## Slide 6
Modal
Requests natural frequencies and mode shapes between 20 Hz and 150 Hz
Forced (modal solution)
Set-up
Forcing frequencies: 20 Hz – 150 Hz, step size = 1 Hz;
Set the appropriate values for the analysis in the Lanczos Data section.
Damping: apply a 0.5% constant damping (critical) at all frequencies.
Loads: use the table constructor to import the .txt files  create 4 frequency excitation sets, then apply a unit load in the +Z direction for each one of them at the corresponding node.
Output
Request the magnitude of the acceleration at nodes 25171, 10445, 20197, 5386

## Slide 7
Plots can be exported by right-clicking on the curve end selecting Export
Axes may be modified by right-clicking on the axis name
Info